## Slide 1: Bike Odometer
Carolyn Mason
ASEN 5519
December 10, 2015

## Slide 2: Project Overview
Sensors:
  Sparkfun Pulse Sensor (Sen 11574)
  Sparkfun Hall Latching Effect Sensor (US1881)
Display ride statistics to user:
  Current Speed
  Average Speed
  Max Speed
  Distance
  Ride Time
  Pulse

## Slide 3: Hardware Schematic
Pulse Sensor
+5V
Output Signal
GND
+5V
GND
Output Signal
+5V, Portable USB
Battery Pack
J10 Pin1, GND
Port A Pin 10, AN11
Port A Pin 11, AN10
Port C
Port B Pin 7, RB7
LCD
LED 1
LED 2
Port B Pin 6, RB6
Port B Pin 5, RB5
PIC18F87K22
LED 3
Hall Effect Sensor
10k Ω

## Slide 4: Physical Hardware

## Slide 5: Software: Overview
Interrupts
Main
Initialize Ports
Set up ADC
Timer0/ interrupts
Initialize LCD
Initialize
Loop
Pulse Sensor
Hall Effect Sensor
Cnt1
Cnt2
Cnt3
Cnt4
Cnt5
Current Speed
Average Speed
Max Speed
Distance
Ride Time
Cnt6
Pulse

## Slide 6: Software: Pulse Sensor
Start
Store ADRES [previous, new]
New > 4000
Previous < 4000
End
Increment counter
Counter > 2^16
Reset counter
Calculate BPM from counter
Save to string

## Slide 7: Software: Hall Effect Sensor
Start
Store ADRES [precious, new]
New > 3000
Previous < 3000
End
Increment counter
Counter > 2^16
Reset counter
Calculate current speed from counter
Save to string
Current speed >0
Calculate
-Average speed
-Max speed
-Ride time
-Ride distance

## Slide 8: Obstacles
Physical connections
  Solution: Watch connections closely when riding and use more tape
Portability
  Solution: Bought a potable charger (5V, 1amp)
Timing resolution
  Solution: Use an oscilloscope to view and measure peaks. Use USART to plot data for easier viewing.